General representation of light in 3D

# Light Source
How to store light source information in computer ?
The project is based on Rendering equation :

From it and after some implementations, we determined that all light sources should have method getNextBeam() from which you can get information „from where to where is beam going“, some information about its color and which light source emitted it. Besides that LS only needs method getNumberOfBeams() which is used for color (power on camera) deduction. With this 2 methods, we can load any valid LS and immediately start using it.

Therefore LS should implement this interface (Java):
interface LightSource extends java.io.Serializable{
Beam getNextBeam();
double numberOfBeams();
}

Beam is data class, and generally looks like this:
public class Beam{
SpatialData sd;
LightSource parent;
ColorData c;
}
Where SpatialData sd is some representation of Beams origin and direction, LightSource parent is reference for LS that generated this beam and ColorData c is another data class, that contains representation of beams color.

In my implementations, I directly replaced SpatialData sd with 2 variables : Vector3 origin and Vector3 direction , and ColorData c with double lambda and double power. To use LS with different beam’s SpatialData sd, you have to Transform it to be compatible with your renderer, which could slow it down significantly (depends on how different are your representations) and besides some representations having less memory requirements then mine (for example Vector3 origin and Double angleA, andlgeB), I thing its better to use faster (all this math needs vectors) 2-vector representation for all LS.

In my implementations, I generate wave lengths with power and not RGB values, because this way, we can easily produce different optical effect just by adding know physical principles into renderer. Down side of this is that it introduces need for SPD2s and little bit of Color science.

If Beam isnt compatible with your renderer, the easiest solution is to wrap it in LS that is. This way you have to transform Beam data only once → when getNextBeam() is called (wrapper returns transformed beam).
# Spectral Power Distribution
Spectral Power Distribution or SPD for short, represents how much energy is illuminated/absorbed/… on each wavelength.

Illustration 1: SPD of flourescent lamp, source: http://www.lrc.rpi.edu/education/learning/terminology/spectralpowerdistribution.asp

In this project, SPDs are used for color deduction and wavelength generations. All SPDs integrals should be equal to 1.
In our interface SpectralPowerDistribution , we have method getNextLamnbda(), which should use SPD for „weighted random distribution“ of lambdas (wavelengths) - wavelength generations.
Then it has getValue(double lmb), which should return SPDs power on wavelength lmb – used for color creation with power obtained form LS.
# Color
Human eyes have 3 cones (S,M,L) which perceive color. They are sensitive to different, overlapping parts of visible light spectrum, and are more sensitive to different wavelengths in their corresponding part of light spectrum. This means that color does not depend only on which wavelengths are hitting your eye, but also on how many fotons with same/different wave length are there.
This is why there are things like CIE standard observer, and why we have interface Color with SPDtoRGB(SPD a) method. It takes SPD and outputs RGB color using ColorScience - it calcualte XYZ from SPD, using cone sensitivity defined in specific implementation of Color, and then it converts XYZ to RGB.

# Math
Using Vectors [x,y,z] (4. value is 1 implicitly) for points, directions and normals, 4x4 row major order matrices for transformations.
# Non uniform distributions
How to turn uniform random distribution to nonuniform random distribution ?
In many cases, we want to create weighted random distribution based on some samples.

Illustration 2: some samples
X is what we want to get, Y is its weight.
That means that we want same amount of 1 as 4, but only half as many 3 as 1 (or 4) and three times more 2 than 3.
Easy solution is to compute the sum of functional values form 1 to 4 of this sample, which is 8, and then produce random number η form [0,1) , multiply it with found sum and then sum functional values until our sum is > η*8. Our random number from this weighted distribution is the last X used in sum. I use sum instead of integral, because we do not care about step size in this case.
Generalization:
We have samples on uniform set {a,...,b} with values of f(x), x ∈ {a,...,b}
1) Calculate I = sum from{n = a} to{b} f( n )
2) Produce i = η * I, η is random number form [0,1)
3) Find greatest r for sum from{n = a} to{r} f( n ) < i where r is our result
Problem with this solution is that it creates “Choppy” distribution,and if we want to fill gaps between two adjacent elements k,l ∈ {a,...,b} so that their f(x) wold be ,for example, linearly changing, we have to add more samples between k,l , what add more iterations.
We can deal with “choppynes” by adding more samples which would reduce “choppynes”, but not in all cases, or by replacing gaps with some function that is easy to integrate which would remove “choppynes” completely.
Example of replacing gaps with linear function:
To find our function gn(x) for gap filling between A and B we will use this formula y - y1 = m*(x-x1). In our case, m = (f(B) – f(A))/(B-A) , y1 = f(A) and x1 = A .
y - f(A) = m*(x – A) is y = {f(B)-f(A)} over {B-A} *( x - A ) + f( A ) let c1 = (f(B) – f(A))/(B-A), c2 = (f(B)*A + f(A)*B)/(B-A) then gn(x) :y = c1*x – c2, x ∈ <A,B) and int g_n(x) = c1 int xdx - c2 int 1dx = (c1) over 2 *x - c2*x = x*( (c1) over 2 -c2) . Now we want to find r from int from{a} to{r} sum from n=a to b g_n(x) *. We can do similar thing as in beginning (but with I equals sum of all gn() integrated), find greatest r1 that sum of all integrals of gn(x) on each ones <A,B) is less than i, and solve int from A to r_2 g_n( x ) = i - r_1*I what is r_2*( c_1 over 2 - c_2 ) -A*( c_1 over 2 - c_2 ) = i -r_1*I where r_2 = ( i-r_1*I )over( c_1 over 2 -c_2 ) + A so r = r1 +r2 .
For highest sped on dense sets, we can precompute all integrals and constants, then just quickly retrieve r1 and constants of next gn and calculate r2.
# Renderer
Right-handed system, x – is horizontal (bottom of monitor), y is vertical, z is depth (exiting from monitor towards viewer is positive value, entering into monitor is negative value)
It will most likely be bidirectional path tracer, with SPD and Power as color representation which enables easy use of known light interaction rules and thus should result in easily created photo-like images.
Renderer will be composed of following elements:
## Scene
Contains SceneObjects, Cameras (CameraManager) and lights	(LightSourceManager), manages light/camera path tracing.
## SceneObject
Something that can interact with beams (light/camera). Provides ray	intersection function, which returns new beam using relevant material	function. Scene should contain SceneObjectManager containing all SO.
## Camera
 Can create image from detected beam data, Can create camera beams,	is aware of “master light source” - LightSourceManager
Scene should contain CameraManager, CameraManager contains all	other sensors (Cameras)
## Light source
 Can create light beams with some color data (wavelength, power ),	knows how many beams created.
Scene should contain 1 LightSourceManager, which contains all other	LS
## Materials
Have material function which takes beam and returns new one